## Router MikroTik CCR1036-12G-4S-EM

## Specifications

| Details |
| --- |
| Product code | CCR1036-12G-4S-EM |
| Architecture | TILE |
| CPU | TLR4-03680 |
| CPU core count | 36 |
| CPU nominal frequency | 1.2 GHz |
| Dimensions | 443 x 193 x 44 mm |
| RouterOS license | 6 |
| Operating System | RouterOS |
| Size of RAM | 8 GB |
| Storage size | 1 GB |
| Storage type | NAND |
| MTBF | Approximately 200'000 hours at 25C |
| Tested ambient temperature | -20°C to 60°C |
| IPsec hardware acceleration | Yes |

## Powering

| Details |
| --- |
| Number of AC inputs | 2 |
| AC input range | 100-240 |
| Max power consumption | 60 W |
| Cooling type | 2 fans |

## Ethernet

| Details |
| --- |
| 10/100/1000 Ethernet ports | 12 |

## Fiber

| Details |
| --- |
| SFP DDMI | Yes |
| SFP ports | 4 |

## Peripherals

| Details |
| --- |
| Serial console port | RJ45 |
| Number of USB ports | 1 |
| USB Power Reset | Yes |
| USB slot type | USB type A |
| Max USB current (A) | 1 |
| Number of M.2 slots | 1 |

## Other

| Details |
| --- |
| CPU temperature monitor | Yes |
| PCB temperature monitor | Yes |
| Voltage Monitor | Yes |
| Mode button | Yes |
| Beeper | Yes |

## Certification & Approvals

| Details |
| --- |
| Certification | CE, EAC, ROHS |
| IP | IP20 |